## Slide 1: Eagle CAD Workshop (1)
Common Rules for Schematic Design

## Slide 2: Common Rules for Schematic Design
Use Component Designators
Clear up text
High Top Low Bottom (HTLB)
Left-to-Right
Common Subcircuits
Direct connections
Visualization
Short and concise names
UPPER CASES
Dots Connects, Crosses Don’t (DCCD)

## Slide 3: Use Component Designators!
Will talk more about this in first few files.
ASME Y14.44-2008 or IEEE 315-1975 How to properly reference and annotate.
To name a few…
  C is for Capacitor
  F is for Fuse
  R is for Resistor
  J is for Jack
  P is for Plug
  Etc…

## Slide 4: Clear Up Text!
If your symbol is pointing like this…
If you happen to rotate your symbol…
Label
Label

## Slide 5: High Top Low Bottom!
High Top
  …Means Higher voltages should placed on top of a schematic
Low Bottom
  …Means Lower voltages should placed on bottom of a schematic

## Slide 6: Left-to-Right
Flow of schematics, regardless of logic or power, should be moving from left to right.
Combined with HTLB, power flow schematics will have general direction of top-left to bottom-right.

## Slide 7: Common Subcircuits!
Which circuit look familiar to you?
If you are deciphering, its bad schematic.

## Slide 8: Direct Connections!
If possible, make direct connections as many as possible.
If size is limited, that is fine; make isolated connection, but…

## Slide 9: Visualization!
…Label your nets if they are ISOLATED!
Any net/wire that are isolated from actual circuit, MUST be labelled to follow.

## Slide 10: Short and Concise Names!
Let’s say a resistor with two different name…
  10k 5% Resistor for current limiting
  R1 10k 5%
Which would look more clear when placed in a schematic

## Slide 11: UPPER CASES!
Obvious reason, this allows components and nets/wires to stick out from schematics.
You can use small cases for comments; just make sure to use UPPER CASES even when you are writing components in comments!
  Component u1 is microcontroller
  Component U1 is microcontroller

## Slide 12: Dots connect, Crosses Don’t
If you see dots between two or more nets, they are connected.
If two or more nets are crossed, they are NOT connected.