## Slide 1: Electronics Workshop (8)
2017 July 7th
Arduino Week (4)

## Slide 2: Files to Cover
Works_012
  Intro to Arduino UART Communication
Works_013
  From Computer To Arduino
Works_014
  Data Parsing Technique (1)
Works_015
  Data parsing Technique (2)
Works_016_a
  Data Parsing Technique (3)
Works_016_b
  Data Parsing Technique (4)

## Slide 3: QUIZ
Bitwise Operators
  &
  |
  ^
  <<
  >>
  ~
(xh <<8) | xl
  Shift xh by 8 bits, then mask with xl
Clear bit pattern 0b11010110 using bit pattern itself
  (~0b11010110) & 0b11010110
Bitwise AND
Bitwise OR
Bitwise XOR
Bitwise LEFT
Bitwise RIGHT
Bitwise NOT

## Slide 4: QUIZ
I2C vs UART?
  Data rate (faster), number of connectible master/slave
I2C vs SPI?
  Data rate (slower), number of connectible master/slave, number of used wires
I2C Data rate range?
  100~400kHz

## Slide 5: QUIZ
Arduino I2C Library has…
  Wire.begin()
  Wire.beginTransmission()
  Wire.endTransmission()
  Wire.write()
  Wire.read()
  Wire.requestFrom()
  Wire.available()

## Slide 6: QUIZ
Refer to LIS3DH Datasheet!
  Data output?
    16-bits
  What are the possible slave addresses for LIS3DH? (There are two!)
    0b0011001, 0b0011000
  Which register is used to check device ID?
    0x0F
  Where are the output registers in memory?
    0x28~0x2D
  Assuming +-4G output, what is the G/LSB value?
    8192

## Slide 7: UART Communication
10 bits for 1 byte
  Start bit
  Bit 0~7 (8 bits, but can be changed)
  End bit
Baud Rate
  Defines data rate
  For example, 9600baud means 9600bits per second (104.166667 microseconds per bit)

## Slide 8: UART Communication
Parity Bits
  Lowest level of error checking.
Even-Parity/Odd-Parity
  Even Parity checks if remainder of sum of all bits reports zero
  Odd Parity checks if remainder of sum of all bits reports one

## Slide 9: UART Communication
9600 8N1
  9600 Bits per seconds
  8 bits data
  No Parity
  One stop bits
115200 8E1
  115200 Bits per seconds
  8 bits data
  Even Parity
  One stop bits