## Slide 1: Eagle CAD Workshop (6)
How to Read: PMIC

## Slide 2: PMIC
Power Management IC
Miniaturized version of voltage regulator
Ideal for small electronics; your microcontroller board
Not so ideal when it comes to high-power requirements.

## Slide 3: What Types?
Two Major Types
  Linear
    Input vs. Output graph has linear characteristic
  Non-Linear
    Boost Topology
    Buck Topology

## Slide 4: Then It Splits Into…
Output Characteristic!
  Fixed Output
    Outputs fixed voltage as long as input voltage sustains.
  Variable Output
    Can adjust output by sending ‘feedback’ voltage back to adjustment pin

## Slide 5: Ready To Get One?
LM2940CT-5.0/NOPB
Things to look for
  Output Configuration
  Output Type
  No. of Regulators
  Max. Input Voltage
  Output Voltage (Fixed)
  Max. Dropout Voltage
  Output Current

## Slide 6: Things To Look For
Output Configuration
  Positive or Negative Output?
Output Type
  Fixed? Adjustable?
No. of Regulators?
  Means number of outputs
Max. Input Voltage
  How high can you input voltage?
Output Voltage
  What is the output voltage?

## Slide 7: Things To Look For (Cont.)
Max. Dropout Voltage
  What is the MINIMUM voltage we must supply?
  1V @ 1A
    Means we need at least (Output)+1V @ 1A to successfully supply 5V, 1A of power.
Output Current
  Max. output current.

## Slide 8: Watch Out For Temperature!
Some PMICs output less power when it gets hot/cold.
Generally, higher the temperature, higher the internal resistance they get.