## Slide 1: Eagle CAD Workshop (3)
How to Read: Diodes

## Slide 2: Diodes
General Purpose
LED
Schottky
Zener

## Slide 3: Common Specs
Forward Voltage
  Voltage required for electrons to go through
  Paired with forward current
  500mV @ 4A
    Means we need at least 500mV (0.5V) to pass 4A
  Expect voltage drop!
    5V 4A -> 4.5V @ 4A

## Slide 4: Common Specs (Cont).
Reverse Leakage
  Amount of current leaking when backward voltage is applied
  Paired with reverse voltage
  6nA @ 6.1V
    Means 6nA will reserve through diode when 6.1V is applied.

## Slide 5: Schottky Diode
Fast recovery time
  Means diode will take less time to drain out electrons sitting inbetween diode
Small forward voltage
  Ideal for high-efficiency circuit (ie. Solar Cells)

## Slide 6: Zener Diodes
Usually used as intentional reverse current conductor
Has very precise breakdown voltage
  Reverse Voltage
  For Zener diodes, its called Zener Voltage
Using its precise breakdown voltage, it is used as voltage reference.