## Slide 1: Eagle CAD Workshop (3)
How to Read: Transistors

## Slide 2: Two Major Types
By now we should know both of them
  BJT (Bi-Polar Junction Transistor)
  FET (Field Effect Transistor)
Also, two major topologies
  NPN (N-Channel for FET)
    BJT: Arrow pointing out
    FET: Arrow pointing in
  PNP (P-Channel for FET)
    BJT: Arrow pointing in
    FET: Arrow pointing out
For simplicity, we will only look at NPN

## Slide 3: NPN BJT
Current Operated
  Enough CURRENT needed to operate
Three pin-outs
  Base: Signal pin to open/close connection between Collector and Emitter
  Collector: ‘Positive’ side
  Emitter: ‘Negative’ side

## Slide 4: BJT Transistor Specifications
VCBO = Collector-Base Voltage
  Maximum voltage between Collector and Base pin
VCEO = Collector-Emitter Voltage
  Maximum voltage between Collector and Emitter pin
VEBO = Emitter-Base Voltage
  Maximum voltage between Emitter and Base pin
ICEX = Collector Cut-off Current
  Maximum current at which Collector cuts-off electrical flow
IBEX = Base Cut-off Current
  Maximum current at which Base cuts-off electrical flow
IC = Collector Current
  Maximum current collector can allow to flow

## Slide 5: 2N3904 Signal NPN Transistor
VCBO = 60V
VCEO = 40V
VEBO = 6V
ICEX = 50nA
IBEX =50nA
IC = 200mA

## Slide 6: N-Channel MOSFET
Voltage Operated
  Enough VOLTAGE needed to operate
Three pin-outs
  Gate: Signal input pin
  Drain: ‘Positive’ pin
  Source: ‘Negative’ pin

## Slide 7: MOSFET Transistor Specifications
VDSS = Drain to Source Voltage
  Maximum voltage between Drain and Source pin
VDGR = Drain to Gate Voltage
  Maximum voltage between Drain and Gate pin
VGS = Gate to Source Voltage
  Maximum voltage between Gate and Source pin
ID = Continuous Drain Current
  Maximum current Drain pin can hold while current flow continuously
VGS(TH) = Gate Threshold Voltage
  Minimum voltage required to close between Drain and Source

## Slide 8: FQP30N06L N-Channel MOSFET
VDSS = 60V
VDGR = 60V
VGS = +10V, -8V
ID = 30A
VGS(TH) = Min. 1V Max. 2V

## Slide 9: Common Parameters
Power Dissipation
  Amount of thermal energy released during operation
  Hotter they get, less amperage they can carry out