## Slide 1: Eagle CAD Workshop (5)
How to Read: Relays

## Slide 2: Relay
Electromechanical Component
Buffed-up transistor, but no polarity
Anatomy of a relay
  Coil
    When current goes through, generates electro-magnetic field, acting as temporary magnet for contact to close
  Contact
    The pathway for actual electrical current.
    Isolated from coil

## Slide 3: What to Read?
Coil Type
  Non-Latching
    Think of momentary switch
  Latching
    Think of push-on push-off switch
Coil Voltage
  Maximum coil voltage to energize coil
Coil Current
  MINIMUM coil current to energize coil
Switching Voltage
  Maximum voltage for contact to operate without problem
Contact Rating
  Maximum current for contact to operate without problem

## Slide 4: NC and NO
If you got a relay that is SPDT
Or you got a relay that is SPST-NO
NO
  Normally Opened
  Contact is in open position when coil is not energized
NC
  Normally Closed
  Contact is in closed position when coil is not energized

## Slide 5: Troubleshooter
Its making clicking sound
  Contact is rapidly opened and closed
  Why?
    Coil is constantly energized-discharged
    If coil is constantly energized-discharged…
    Means either current is varying or…
    Voltage is dropping