## Slide 1: Eagle CAD Workshop (2)
Passive Components

## Slide 2: Resistors
Anything that limits current
, or
Watch for power rating!
Resistance, Tolerance, Power, and Composition
  Resistance: Color coded
  Tolerance: ±5%, etc.
  Power: 1/4W, 0.25W, etc.
  Composition: Metal film, carbon film, etc.

## Slide 3: Capacitors
Very very tiny battry
Polarized and Non-polarized
  Check where to connect for polarized!
Ceramic, Tantalum, Aluminum
  Ceramic: All-arounder, but bad capacitance.
  Tantalum and Aluminum: Polarized, packed with capacitance, but not so easy to handle.
Capacitance, tolerance, voltage rating

## Slide 4: Inductors
Coil wrapped around core
Inductance, tolerance, current rating, current saturation
Current Saturation!
  Point where inductor CANNOT generate any more electromagnetic field.
  Coil starts to heat up.
  Still, your coil will physically survive as long as it is less than current rating.