## Slide 1: Electronics Workshop (13)
Arduino Week (7)

## Slide 2: Files to Cover…
Works_019
  All about memories
Works_020_a
  EEPROM
Works_021
  Saving memory through F() macro
Works_020_b
  Heap and dynamic allocation

## Slide 3: The Memory Bar
Inside the ATmega chip, we have…
  FLASH Memory
  SRAM
  EEPROM
For Arduino Mega…
  256 KB of FLASH, 8KB for Bootloader
  8 KB of SRAM
  4 KB of EEPROM
FLASH
EEPROM
SRAM

## Slide 4: The SRAM Bar
Static Data
  Data which will remain at the end of program.
Stack
  Local variables and function calls
  Calling functions DO consume memory!
Heap
  Dynamically allocated data
  Functions do create variables via heap
Free Space
Heap
Static Data
Stack