## Slide 1: Eagle CAD Workshop (7)
How to Read: Microcontrollers

## Slide 2: Microcontrollers
What we’ve been working with is called SoC; System on Chip.
  To be defined as SoC
    1. CPU
    2. RAM
    3. ROM
    4. Secondary Memory Device (Flash)
    5. Input/Output Device
  All you need to do; apply power and program.

## Slide 3: If It is NOT SoC…
Means you need to connect devices together to make them fully functional.
  Your desktop
  Your laptop
Nowdays, definition for SoC is lightened up a bit
  Raspberry Pi: No secondary storage, but still counts as SoC

## Slide 4: Now to Pick Your Partner…
We will reference Atmega 328P
  One used in Arduino Uno!
Thinks to look at
  Core Size
  Clock Speed
  Throughput
  Memory Storage

## Slide 5: Core Size
8-bit
  Means single command takes up 8-bits of space
    1 byte
  Bigger the core size, more numbers you can hold
  For 8-bit, its 2^8 (256)

## Slide 6: Clock Speed
Assuming clock is generated by external clock device (Resonator)
20MHz
  Means microcontroller will perform single instruction within 50ns.
  Tightly connected with processor’s processing throughput

## Slide 7: Throughput
Number of tasks completed per unit time.
  20MHz clock speed, remember?
  50ns per single instruction…
  20,000,000 instructions per second!
  Also known as 20MIPS (Million Instructions per Seconds)

## Slide 8: Memory Storage
Bigger the memory, more data you can hold while its running
Remember the crazy memory management session in Arduino?
For 328P, 2KB of SRAM

## Slide 9: Other Things to Look for…
ADC
  Look for resolution!
  10-bit ADC
    1023 in decimal
    For example, a 360 degree rotating sensor…
    360/1023 = 0.3519061583577713 deg/bit
Communication Interfaces
  USART
  SPI
  I2C

## Slide 10: But Above All…
Power Consumption!
Operating Voltage!
Speed Grade!
Number of I/O pins!